## Slide 1: Running PrimeTime
Setting up the environment and running a static timing analysis in Synopsys PrimeTime (pt_shell)
Notes: Companion to the 3-day STA ramp-up plan (Day 2: running STA). Commands are taken from public university PrimeTime labs and Synopsys material; exact syntax and options vary by PrimeTime version, so confirm with man pages in pt_shell.

## Slide 2: What goes in, what comes out
Netlist
Gate-level Verilog (.v) from synthesis or P&R
Libraries
Compiled timing libraries (.db)
Constraints
SDC: clocks, I/O delays, exceptions
Parasitics & delays
SPEF (RC), optionally SDF
Reports
setup.rpt, hold.rpt
violators (violate.rpt)
clock skew (skew.rpt)
saved session to reload
Notes: Inputs and report names from the LTH PrimeTime lab slides (netlists/: .v .sdf .spef .sdc; reports/: setup.rpt hold.rpt violate.rpt skew.rpt). Session save/restore from the velog Synopsys lab notes.

## Slide 3: Set up the working area
Project layout
project/
netlists/ .v .sdf .spef .sdc
scripts/ .tcl
reports/ setup, hold, skew
.synopsys_pt.setup
Your site may provide an init script that creates this layout and sets the tool path (one lab uses inittde).
Setup scripts
.synopsys_pt.setup
Hidden file in the run directory; holds library paths and aliases
Reference-methodology scripts
common_setup.tcl (shared with DC and ICC), pt_setup.tcl (PT settings), pt.tcl (your run and checks)
Notes: Layout and init script: LTH PrimeTime lab slides. .synopsys_pt.setup and the RM file split (common_setup.tcl, pt_setup.tcl, pt_scripts/pt.tcl): velog Synopsys lab notes and the UT Austin standard-cell PrimeTime tutorial.

## Slide 4: Point PrimeTime at the libraries
# in .synopsys_pt.setup or pt_setup.tcl
set search_path "<lib path> <design path>"
set link_library "* design.db"
set target_library "design.db"
# confirm inside pt_shell
printvar search_path
printvar link_path
list_libraries
report_lib
search_path
Directories searched for libraries and design files
link_library / link_path
Libraries used to resolve cells; "*" means designs already in memory
list_libraries, report_lib
Check the right .db files actually loaded
Notes: set lines from the LTH lab slides; printvar/list_libraries/report_lib from the velog lab notes. The LTH slides use link_library; the velog notes print link_path (PrimeTime's name for the link list). Check which your version expects with man link_path.

## Slide 5: Three ways to launch
Interactive shell
pt_shell
# 64-bit on some sites:
pt_shell -64bit
Type commands, or source a script
Batch with a log
pt_shell -f run.tcl \
| tee -i run.log
Runs the whole script and keeps the log
GUI
pt_shell
start_gui
Visual path and schematic browsing
Notes: pt_shell -64bit and start_gui: LTH lab slides. pt_shell and source <script>: UT Austin tutorial. -f run.tcl | tee -i run.log: velog lab notes.

## Slide 6: The run flow in six steps
1
Load design
read_verilog, current_design, link_design
2
Parasitics
read_parasitics (SPEF), read_sdf
3
Constraints
read_sdc, then operating conditions
4
Check
check_timing, parasitic annotation
5
Report
report_timing, violator report
6
Save & signoff
Save session, restore, iterate
Parasitics matter most at current nodes, where net delay dominates. Steps 3–5 loop until timing is clean.
Notes: Order (design → parasitics → constraints → update/report/analyze with save and restore → signoff) from the velog lab notes. Commands from the LTH lab slides and velog notes.

## Slide 7: A minimal run script
# 1 Load design
read_verilog top_level.v
current_design "top_level"
link_design
# 2 Parasitics and delays (post-layout)
read_parasitics -format SPEF top_level.spef.gz
read_sdf top_level.sdf
# 3 Constraints and corner
read_sdc top_level.sdc
set_operating_conditions <worst | best>
# 4 Check
check_timing
report_annotated_parasitics
# 5 Report
report_timing -delay max \
-path full_path -max_paths 10 \
> reports/setup.rpt
report_timing -delay min \
> reports/hold.rpt
report_constraints -all_violators
Notes: Assembled from commands shown in the LTH PrimeTime lab slides (worst case for setup, best case for hold) and the velog notes. <worst | best> is a placeholder for your library's operating-condition names. Redirect with > as in standard pt_shell Tcl usage shown in the lab's power example.

## Slide 8: Sanity checks before trusting slack
check_timing
Flags missing constraints, such as unconstrained outputs
report_annotated_parasitics
Shows how many nets got RC values; "not annotated" nets can't be trusted
report_exceptions -ignored
Lists false/multicycle paths the tool ignored
report_analysis_coverage
Shows which timing checks were actually analysed
list_designs, current_design
Confirms the right top design is linked
Notes: All five from the velog Synopsys lab notes. Ties to playlist Week 6 Video 1 (check_timing clean) and Week 5 Videos 6–7 (netlist log, parasitics report).

## Slide 9: Reading the main reports
Command / option | What you get
report_timing | Worst path by default
-delay max ¦ min | Setup (max) or hold (min)
-path full_path | Full path detail
-max_paths <n> | Paths per group (default 1)
-from … -to … | Limit to start and end points
report_constraints -all_violators | All setup, hold and DRC violations
report_clock_timing -type skew -verbose | Clock skew
Notes: Options and defaults from the LTH lab slides. Report types endpoint / full / full clock expanded are covered in playlist Week 6 Video 4; check report_timing -path options in your version's man page.

## Slide 10: Iterate with sessions, then scale up
Save and restore
A saved session is a directory you can reload instead of re-reading everything
Sessions are tied to the PrimeTime version that wrote them
Typical loop: edit pt.tcl, rerun, compare reports
Beyond a single run
Distributed multi-scenario and multi-corner analysis
Crosstalk (PrimeTime SI), AOCV / POCV
PBA accuracy at GBA runtime (HyperTrace)
Physically-aware ECO guidance
Notes: Session behaviour from the velog lab notes (exact save_session/restore_session syntax not shown there; check man pages). Advanced features from the Synopsys PrimeTime product page and datasheet; see Day 2–3 of the ramp-up plan.

## Slide 11: Caveats & sources
Commands come from public university labs, not Synopsys's own user guide (that needs a SolvNet login).
Syntax and options vary by version; run man <command> in pt_shell to confirm.
Paths, library names and operating conditions are placeholders for your site's values.
Sources: Lund University (LTH) ETIN35 PrimeTime slides · UT Austin CERC standard-cell PrimeTime tutorial · velog "SYNOPSYS DAY10" PrimeTime lab notes · Synopsys PrimeTime product page and datasheet · Bhasker & Chadha, Static Timing Analysis for Nanometer Designs, Ch. 7–8