## Slide 1: STA Ramp-Up: 3-Day Plan
Static Timing Analysis, from where STA fits to full-chip signoff — mapped to the STA Series playlist (Chip Design with Rashid)
Notes: Condensed from a 12-week research plan into three days. Built on one core textbook (Bhasker & Chadha, Static Timing Analysis for Nanometer Designs), the Liberty User Guide, and tool documentation. Every playlist video provided by the user is mapped to a session.

## Slide 2: Three days, three layers
Day 1
Playlist Weeks 1–5
Foundations & inputs
Where STA fits in PD
Core timing checks
Libraries, netlist, SPEF
Day 2
Playlist Weeks 6–9
Running STA
Flow, SDC, check_timing
Timing report types
GBA vs PBA, MMMC
Day 3
Playlist Weeks 10–12
Margins & full chip
Modes, derates, OCV
Block-to-block timing
Crosstalk, CRPR/CPPR

## Slide 3: Day 1: Foundations & inputs
Session 1 · Morning
Why STA, where it fits
STA complexity challenge
Hierarchical chip planning
PD stages: synthesis → routing
Signoff STA, inputs & outputs
Session 2 · Midday
Core timing checks
Timing arcs & unateness
Setup, hold & slack
Path types: in-reg, reg-reg, reg-out
Skew, latency, uncertainty
Session 3 · Afternoon
Libraries & parasitics
Read a .lib: NLDM vs CCS/ECSM
Wire-load → extracted SPEF
Reviewing the read-netlist log
SPEF format & parasitics report
Notes: Lab: install OpenSTA, load a sample design and run report_checks; compare timing with and without SPEF and inspect delay calculation with report_dcalc. Sources: Bhasker & Chadha Ch. 1–5 and App. C; Liberty User Guide; OpenSTA README; Week 2 Video 1 description.

## Slide 4: Day 1: playlist & reading
Playlist video | Session | Read
STA Series, Week 1, Video 1: Static Timing Analysis - Complexity Challenge | 1 | B&C Ch. 1
STA Series, Week 1, Video 3: Hierarchical Planning of the Chip | 1 | B&C Ch. 1
STA Series, Week 2, Video 1: Overview of Physical Design Stages and where STA fits | 1, 2 | B&C Ch. 1–2, Ch. 8
STA Series, Week 5, Video 6: Review Read Netlist Log File (Members only) | 3 | B&C Ch. 3; tool guide
STA Series, Week 5, Video 7: Understand SPEF Format & Review Parasitics Report (Members only) | 3 | B&C Ch. 4–5, App. C
Notes: Session 2 covers core concepts from the research plan; no specific playlist video was supplied for it. B&C = Bhasker & Chadha, Static Timing Analysis for Nanometer Designs.

## Slide 5: Day 2: Running STA
Session 1 · Morning
Flow & constraints
Basic STA flow revision
Getting check_timing clean
SDC: clocks, I/O delays
False & multicycle paths
Session 2 · Midday
Reading timing reports
Report types: endpoint
Full path report
Full clock expanded
Lab: report_checks in OpenSTA
Session 3 · Afternoon
Analysis modes
GBA vs PBA: pessimism vs runtime
Concurrent multi-mode multi-scenario runs
How PrimeTime & Tempus do each
Notes: Sources: Bhasker & Chadha Ch. 7, Ch. 8, Ch. 10, App. A (SDC); PrimeTime datasheet (HyperTrace: PBA accuracy at GBA runtime, distributed multi-scenario); Tempus datasheet (distributed PBA, concurrent MMMC).

## Slide 6: Day 2: playlist & reading
Playlist video | Session | Read
STA Series, Week 6, Video 1: Revision - Basic Static Timing Analysis flow, Check_Timing clean | 1 | B&C Ch. 7, App. A
STA Series, Week 6, Video 4: Report Timing types - endpoint, full, full clock expanded | 2 | B&C Ch. 8; tool guide
STA Series, Week 7, Video 5: GBA vs PBA - Path Based Analysis | 3 | B&C Ch. 10; PT/Tempus docs
STA Series, Week 8, Video 4: Concurrent Multi Mode Multi Scenario Run (Members only) | 3 | B&C Ch. 10; PT/Tempus docs
Notes: Session 1's SDC content (Week 9 had no supplied video) follows B&C Ch. 7 and App. A.

## Slide 7: Day 3: Margins & full chip
Session 1 · Morning
Modes & margins
Timing modes
Clock uncertainty & derates
Operating conditions, fixed derates
Flat OCV → AOCV → POCV → LVF
Session 2 · Midday
Full-chip timing
Block-to-block timing at top
Paths across top-level clocks
Hierarchical models: ETM, ILM
Session 3 · Afternoon
Crosstalk & pessimism
Crosstalk delay on clock segments
CRPR / CPPR
CPPR with derates & crosstalk
Notes: Sources: Bhasker & Chadha Ch. 6 (crosstalk), Ch. 7, Ch. 9, Ch. 10 (OCV, CPPR, MMMC, SSTA); Liberty User Guide LVF section; SemiEngineering LVF article; Tempus datasheet (ETM/ILM/SmartScope).

## Slide 8: Day 3: playlist & reading
Playlist video | Session | Read
STA Series, Week 10, Video 1: Timing Modes | 1 | B&C Ch. 7
STA Series, Week 10, Video 2: Timing Margin - Clock Uncertainty and Derates (Members only) | 1 | B&C Ch. 7, Ch. 10
STA Series, Week 11, Video 3: Operating Conditions and Fixed derates (Members only) | 1 | B&C Ch. 3, Ch. 10
STA Series, Week 11, Video 6: Full Chip Timing P2 - Block to Block timing at full chip | 2 | B&C Ch. 9–10
STA Series, Week 12, Video 1: Full Chip Timing P3, timing paths across different top level clocks (Members only) | 2 | B&C Ch. 8–9
STA Series, Week 12, Video 2: Full Chip Timing, Impact of Crosstalk delay on Full Chip Clock Segment | 3 | B&C Ch. 6
STA Series, Week 12: Explanation of CRPR/CPPR with derates and Crosstalk | 3 | B&C Ch. 6, Ch. 10

## Slide 9: Six kinds of STA constraints
Clock definition
create_clock
create_generated_clock
Clock characteristics
set_clock_latency · set_clock_uncertainty
set_clock_transition · set_propagated_clock
set_clock_groups · set_clock_sense
I/O & environment
set_input_delay · set_output_delay
set_driving_cell · set_input_transition
set_load
Timing exceptions
set_false_path · set_multicycle_path
set_max_delay · set_min_delay
set_disable_timing
Design rules (DRC)
set_max_transition
set_max_capacitance
set_max_fanout
Modes & analysis control
set_case_analysis · set_operating_conditions
set_timing_derate · set_data_check
group_path
Notes: Grouping is a learning aid; the SDC standard lists commands without categories. Command sources: Microchip SDC command reference; AMD Vivado UG903 supported SDC commands (SDC 1.9 list); SDC notes (akiitr); LTH PrimeTime lab slides; Bhasker & Chadha Ch. 7 and App. A. set_timing_derate is applied in the STA tool (Day 3 derates topics).

## Slide 10: What each constraint tells the tool
Constraint | What it tells the tool | Plan
create_clock / create_generated_clock | Defines clocks: period and waveform on a port or pin, or a clock derived from another | Day 2 · S1
set_clock_uncertainty / latency | Margins for jitter and skew; source and network clock delay before CTS | Day 3 · S1
set_clock_groups | Declares clocks that never time against each other (e.g. asynchronous) | Day 3 · S2
set_input_delay / set_output_delay | Arrival time at inputs and required time at outputs, relative to a clock | Day 2 · S1
set_driving_cell / set_load | Models the drive of external logic and the load on outputs | Day 2 · S1
set_false_path / set_multicycle_path | Removes paths from analysis, or allows more than one cycle | Day 2 · S1
set_max_transition / capacitance | Design-rule limits on slew and load | Day 1 · S3
set_case_analysis | Ties pins to constants to select a timing mode | Day 3 · S1
Notes: Check constraints before trusting results: check_timing flags missing constraints (e.g. unconstrained outputs) and report_exceptions -ignored lists exceptions the tool dropped. PrimeTime also offers SDC consistency checking. Read: Bhasker & Chadha Ch. 7 and App. A.

## Slide 11: Timing analysis in each tool
Tool | Role | Timing analysis supported
Synopsys PrimeTime | Golden signoff | SI, AOCV/POCV, moments; PBA via HyperTrace; multi-scenario/corner; ECO; IR, thermal, aging-aware
Cadence Tempus | Signoff | SI, SOCV/LVF; concurrent MMMC; distributed PBA; ETM/ILM/SmartScope; ECO; IR-aware with Voltus
Fusion Compiler / ICC II | Implementation | PrimeTime delay calc; exhaustive PBA; signoff ECO
Genus / Innovus | Synthesis / P&R | Concurrent MMMC (Genus); threaded MMMC (Innovus); Tempus integration
Siemens Aprisa | P&R | MCMM timing; OCV methods incl. LVF
OpenSTA / OpenROAD | Open source | Liberty, SDC, SDF, SPEF; setup/hold, exceptions — the free lab tool
Ansys Path FX | Path specialist | SPICE-accurate path-based timing; corner & statistical results
Notes: From vendor product pages and datasheets (PrimeTime, Tempus, ICC II, Genus/Innovus, Aprisa fact sheet), the OpenSTA README and the Ansys Path FX page. Features not listed were not found in those sources, which does not mean they are unsupported. Speed and accuracy figures are vendor claims.

## Slide 12: Modelling stack: basic → accurate
Cell delay
NLDM
CCS / ECSM
Interconnect
Wire-load
Extracted SPEF
Variation
Flat OCV
AOCV
POCV/SOCV
LVF
Noise / SI
Crosstalk windows
CCS noise
Abstraction
ETM
ILM
SmartScope
Constraints & annotation
SDC
SDF
Notes: Each step to the right trades runtime and library size for accuracy and less pessimism. CCS: Synopsys claims within 2% of HSPICE. LVF adds early/late sigma tables per timing arc; Liberty 2017.06 adds moments for non-Gaussian distributions. Sources: Bhasker & Chadha Ch. 3–6, 10; Liberty User Guide; Synopsys/Si2 releases; SemiEngineering; Tempus datasheet.

## Slide 13: One core reading set for all three days
Bhasker & Chadha
Static Timing Analysis for Nanometer Designs (Springer, 2009)
Day 1: Ch. 1–5, App. C · Day 2: Ch. 7–8, 10, App. A · Day 3: Ch. 3, 6–10
Liberty User Guide
Liberty User Guides and Reference Manual (2017.06)
Day 1: NLDM, CCS cell models · Day 3: LVF and moments
Your tool's documentation
PrimeTime or Tempus datasheets & user guide; OpenSTA README
Day 2: report_timing, PBA, MMMC · Day 3: hierarchical models, ECO
Notes: Recommendations kept to one book plus two references so the same sources serve every topic. Optional companion playlists from the same channel: Master Timing Constraints, Latch Timing Demystified, Full Chip Timing/STA closure, STA Q&As, Statistical Timing Analysis (SSTA).

## Slide 14: Caveats & sources
Videos are mapped by title only; their content was not transcribed.
Playlist weeks 3, 4 and 9 had no supplied video; those topics come from the research plan.
Members-only videos need a channel membership.
Speed and accuracy figures are vendor claims, not independent benchmarks.
Sources: Bhasker & Chadha (Springer, 2009) · Liberty User Guide 2017.06 · Synopsys PrimeTime page & datasheet · Cadence Tempus, Genus, Innovus datasheets · Synopsys ICC II datasheet · Siemens Aprisa fact sheet · OpenSTA (GitHub) · Ansys Path FX · SemiEngineering (LVF validation) · Microchip & AMD UG903 SDC references · EE Times / EDN (CCS, ECSM) · chipdesignrashid.github.io · YouTube: Chip Design with Rashid